## Slide 1
CHASSIS AND ERGONOMICS
DESIGN
REPORT
PRV 20

## Slide 2
INDEX
1
OVERALL DESIGN CONCEPT
Department ODC …........................................ 1
2
DESIGN CONSTRAINTS
Suspension Geometry …................................. 3
Powertrain Packaging …................................. 3
Driver Ergonomics …...................................... 4
FSAE Rules …................................................. 5
Material Properties Graph ….......................... 6
MATERIAL SELECTION
3
4
FORCES ON THE CHASSIS
Longitudinal Torsion …................................. 7
Vertical Bending …........................................ 7
Lateral Bending …......................................... 8
Horizontal Lozenging …................................ 8
5
6
TORSIONAL STIFFNESS
FINITE ELEMENT ANALYSIS
Calculation Method ................................ 9
Boundary Conditions ….......................... 10
Results …................................................. 11
Engine Mount Analysis …....................... 12
7
MODAL ANALYSIS
Introduction …........................................ 13
Tabular Results …................................... 13
Conclusions …........................................ 14
Comparison ….........................................15
8
ENGINE VIBRATION REDUCTION
Engine Vibration Reduction .................. 16
1
FMEA
FMEA …......................................................... 2
9
TRIANGULATION
Triangulation ......................................... 17

## Slide 3
INDEX
10
SUSPENSION MOUNTING POINTS
Mounting Method …............................. 18
ERGONOMIC JIG
SEAT DESIGN
Ergonomic Parameters …..................... 21
Manufacturing ….................................. 22
Driver Data ........................................... 23
Design Parameters ............................... 24
Design ….............................................. 25
Manufacturing .................................... 26
Seat Insert …........................................ 27
11
12
STEERING WHEEL
PADDLE SHIFTERS
DASHBOARD
Steering wheel Design ....................... 28
Manufacturing .................................. 30
Steering Wheel Display …................. 31
Steering Wheel Comparison............... 32
Paddle shifter Design ....................... 33
Manufacturing ................................. 34
Paddle shifter Comparison................ 35
Dashboard Design ........................... 36
Calculation of Height ...................... 37
PEDAL ASSEMBLY
Pedal Assembly Design .................... 38
16
15
14
13
17
FUTURE GOALS
Future Goals ..................................... 40
10
CHASSIS MANUFACTURING
Manufacturing Process .......................... 19
10
ERGONOMICS OVERVIEW
Manufacturing Process .......................... 20

## Slide 4
DEPARTMENT ODC
To design a car with a frame which is rigid in bending as well as lightweight and which provides optimum comfort and assist the driver to achieve its peak performance
1
Chassis
Minimum Tubes
Maximum Triangulation
Optimum Nodes
Ergonomics
Comfortable Cockpit Design
Optimum Field of Vision
Adjustable Cockpit
Goals:

## Slide 5
FMEA
Item/Function | Function | Potential Failure Modes | Potential Effects of Failure | SEV | Potential Causes of Failure | OCC | Current Design Controls (prevention) | Current Design Controls (selection) | DET | RPN | Recommendation Action
Chassis | To mount the components on vehicle and support | Linkages are not welded properly | Leads to excess vibrations which may lead to breakage of members | 4 | When proper welding type is not studied or welding not done properly | 3 | Various welding techniques were studied and TIG welding was chosen | Reliability test | 2 | 24 | Using proper welding method for joining tube , analysis strength of welding tensile testing machine , or having non-destructive testing of weld cracks
 | The loads in different conditions | Improper choice of material type | Leads to undue flexing and deflection | 2 | Improper material analysis in FEA software | 2 | Material chosen after performing different physical test and comparing with baseline steel | Physical Property testing Physical Property testing | 3 | 12 | Analysing all the material taken into design consideration with proper boundary conditions in simulation
 |  | Structure not properly triangulated | Improper load transfer may lead to the high stress concentration in some regions | 3 | Chassis designing not done properly | 2 | Best possible triangulated sections were considered | After performing multiple Iterations | 3 | 18 | Taking into consideration all possible arrangement of members for obtaining optimum load paths
Seat and seat inserts | To support the driver and provide safety | Frame failure of seat | Driver safety compromised | 5 | Excessive loads | 2 | Using Design guides as reference | Durability and Reliability Test | 4 | 40 | Selection of proper material with required critical bearing stress
Paddle Shifters | For upshifting and downshifting of gears | Improper selection of magnets | Improper retracting mechanism | 3 | Magnetic range not analysed properly | 2 | Various magnet samples were tested, and their strength was analysed. Two neodymium magnets gives the best result | Durability Test | 3 | 12 | Proper analysing the magnetic range. Finding the range up to which magnetic effect can be sensed.

## Slide 6
DESIGN PROCESS
DESIGN CONSTRAINTS:
1
SUSPENSION GEOMETRY
Suspension pickup points
Bell crank mounting points
Damper mounting points
ARB mounting points
2
POWERTRAIN AND DRIVETRAIN PACKAGING
Engine accommodation and mounting
Cooling and Lubrication Routing and mounting
Spool and its mounting
Ease of assembly and disassembly
Decides the rear length of the chassis
3

## Slide 7
3
DESIGN CONSTRAINTS:
DRIVER ERGONOMIC
Cockpit Parameters based on drivability of each driver
Dimensions of the chassis to accommodate all drivers
Ease of egress
Optimum visibility in the front of the vehicle
Driver jig
Mankind Assembly based on anthropometric data
Plot of Driver Anthropometric Data
4

## Slide 8
DESIGN CONSTRAINTS:
4
FSAE Rules
Cockpit Opening Template
95th Percentile Template
Decides the front length of the chassis
Internal Cross-section Template
5

## Slide 9
AISI 1020
1339 Nm2
AISI 4130
1372.475 Nm2
AA 6061-T6
461.286 Nm2
AISI 304
AISI 4140
AA 7075-T6
1292.135 Nm2
1339.01 Nm2
480.035 Nm2
MATERIAL SELECTION
AISI 4130 (chromoly) is selected as a material for chassis production taking into consideration manufacturing parameters – machinability, weld ability.
Flexural rigidity for different materials are specified for a tube of 25.4 mm outer diameter and 1.2 mm thickness:
Flexural Rigidity:
6

## Slide 10
VARIOUS FORCES ACTING ON RACE CAR CHASSIS
1
2
LONGITUDINAL TORSION
VERTICAL BENDING
During Cornering
Major contribution to Force
Due to weight of driver, engine and other components mounted to the frame
7

## Slide 11
3
LATERAL BENDING
4
HORIZONTAL LOZENGING
VARIOUS FORCES ACTING ON RACE CAR CHASSIS
Due to road camber, side wind loads, and centrifugal forces caused by cornering
Due to uneven forces on adjacent tires
8

## Slide 12
TORSIONAL STIFFNESS CALCULATION
9
Finite element model of Chassis was constructed in ANSYS Mechanical APDL 18.1 and 20.1 student version.

## Slide 13
CONDITION 2:
Front portion of the chassis is fixed; couple is applied on the rear suspension pick up points
CONDITION 1:
Rear portion of the chassis is fixed; couple is applied on the front suspension pick up points
10
BOUNDARY CONDITIONS

## Slide 14
RESULTS
TORSIONAL STIFFNESS: 2274 Nm/deg
CONDITION 1
CONDITION 2
11
Displacement in Y direction

## Slide 15
ENGINE MOUNTS ANALYSIS
BOUNDARY CONDITION:
The front and rear bulkhead were fixed and a load of 400N was applied on the four engine mounts.
Displacement in Y direction
12

## Slide 16
When perturbed, any solid body will vibrate at its natural frequency
Analysis of the frame's response under vibration
Stiffness to Weight Ratio determined
Harmonic | Frequency
1 | 0
2 | 0
3 | 0
4 | 1.3911E-04
5 | 3.4997E-04
Harmonic | Frequency
6 | 6.0346E-04
7 | 37.271
8 | 57.157
9 | 69.100
10 | 82.752
13
MODAL ANALYSIS
Natural Frequencies:

## Slide 17
7th mode correspond to twisting motion along longitudinal axis of chassis
8th mode correspond to the longitudinal flexure
Important for longitudinal and flexural rigidity
7th Order Mode Shape
8th Order Mode Shape
14
MODAL ANALYSIS

## Slide 18
Larger value at each harmonic
Better Triangulation
Better design
Additional analysis was done by removing the extra supporting tubes at the rear engine mounts.
Harmonic | Frequency
7 | 37.271
8 | 57.157
9 | 69.100
10 | 82.752
Harmonic | Frequency
7 | 37.214
8 | 55.906
9 | 68.870
10 | 82.649
15
MODAL ANALYSIS
Harmonic values without engine mounts supporting tubes:
Harmonic values with engine mounts supporting tubes:

## Slide 19
ENGINE VIBRATION REDUCTION
16
Primary source of vibrations in the chassis is from the engine
Large vibratory forces are transferred from the engine into the chassis
In the two previous chassis designs, the frame suffered weld joint failures near the engine.
PU Bushing

## Slide 20
TRIANGULATION
Proper triangulation to transfer the loads to different members to minimise stress concentration
17

## Slide 21
SUSPENSION MOUNTING POINTS
Only Tensile and Compressive forces act on the brackets
Tabs are welded at the junction of three or more tubes. These will prevent bending loads and provide load transfer to chassis
18
Shear Force on brackets and bending of brackets prevented
Brackets carrying suspension loads designed on the axes of linkages

## Slide 22
CHASSIS MANUFACTURING
Each chassis member is supported at atleasttwo points to maintain its orientation
Each chassis member is supported at atleasttwo points to maintain its orientation
Separate fixtures for suspension tabs to obtain precise angle and orientation
19
Fixture supports 8 tubes thus reducing the number of fixtures to be welded
Followed DFMA principles

## Slide 23
ERGONOMICS OVERVIEW
20
Ergonomic Jig
Seat
Steering Wheel
Paddle Shifters
Dashboard
Pedal Assembly

## Slide 24
21
ERGONOMIC PARAMETERS
Seat Back Angle
Thigh Angle
Steering Wheel Location
Roll Hoops Location
Dashboard Height and Angle
Pedal Height and Position
Length and Width of Cockpit

## Slide 25
ERGONOMIC JIG
22
Adjustable driver jig to incorporate data for all drivers for cockpit design
Stable support using mild steel tubes ensured correct data collection
Stable wooden support ensured correct seat, back, thigh angles and pedal position

## Slide 26
Adjustable driver's jig
Optimum driver data
Better cockpit design
23
Optimum driver data for chassis design
Back and Thigh Angles
COCKPIT DESIGN

## Slide 27
SEAT DESIGN PARAMETERS
To accommodate all the drivers at their preferred driving position Driver Jig data and 95th Percentile male data were referred to decide the following seat parameters.
1
2
3
4
5
6
SEAT HEIGHT
ARMREST HEIGHT, LENGTH AND LATERAL LOCATION
LOCATION OF DRIVER HARNESS BELTS
SEAT BEACK ANGLE
LUMBAR AND FORE AFT SUPPORT
SEAT CUSHION ANGLE AND HEIGHT
24

## Slide 28
SEAT DESIGN
25
Reclined seat angle at 490 with the horizontal
Comfortable driving position
Lower CG of vehicle – Possible increase in lateral acceleration
Thigh angle is at 300 to provide thigh support

## Slide 29
26
SEAT MANUFACTURING
Finished Seat
Seat just after demoulding

## Slide 30
1
2
3
PROVIDE RAISED HEIGHT
ACCOMMODATE DRIVERS OF DIFFERENT STATURES
PROVIDE CUSTOMIZED LUMBAR SUPPORT
27
SEAT INSERT

## Slide 31
Turn wheel without elbows hitting legs
Upper arm and forearm at 900
Operate Paddle shifters without steering wheel contact
STEERING WHEEL DESIGN
28
Goals

## Slide 32
29
Acquiring information available
Processing the sensed information to understand the situation
Selecting what to do
Executing the response
RPM indicator
lights
Slow and fast clutch release buttons
LCD display showing TPS, BPS, Engine temperature and RPM
Elastic grips of TPU material
Magnetically actuated paddle shifters

## Slide 33
Steering Wheel
TPU grips
FDM 3D printed
TPU
Electronic Panel
FDM 3D printed
Steering Wheel Baseplate
Lasercut
ABS
Aluminium
STEERING WHEEL MANUFACTURING
30

## Slide 34
Steering wheels mounted on car
31
STEERING WHEEL DISPLAY
Cone receptors specialized in detecting red, green and blue
Red colour persists for maximum time
Blue colour has largest peripheral region

## Slide 35
STEERING WHEEL COMPARISON
32
Last Season | Current Season | Goals Achieved
Absence of 3D LCD display for driver assistance | LCD display for better drivability | Enhanced Drivability
Packaging of electrical components was the major issue | Incorporating 3D printed enclosure to accommodate electrical components | Improved Packaging and Ease of Assembly
Absence of compromised driver's comfort | 3D printed grips made of TPU material for driver compfort | Lightweight
Last Season
Current Season

## Slide 36
PADDLE SHIFTERS
Paddle shifters were designed to reduce driver effort and improve shifting time.
Shifters were designed with driver inputs on steering wheel and the position of shifters were made to improve ease of shifting even while cornering
33
Customised paddle shifter design
Magnetic actuated paddle shifters mounted on Steering wheel

## Slide 37
The paddle shifters consists of three parts that are 3D printed. Two neodymium magnets were incorporated.
Paddle was made to pivot about a point and two magnets were pasted on upper and lower parts of paddle and housing respectively
34
Neodymium Magnets
Paddle Housing
Paddle
Shifting Switch

## Slide 38
PADDLE SHIFTER COMPARISON
35
Last Season
Current Season
Last Season | Current Season | Goals Achieved
Retracting mechanism using springs | Retracting mechanism using magnets | Improved Reliability
Torsional spring was under tension all the times therefore had limited life and had to be replaced regularly | Usage of magnets resulted in increased life cycle of the part | Optimised Efficiency
Fixing the spring inside to pivot the paddle was a big issue and retracting was not efficient | Easy fixing of the system since magnets are used and resulted in better retracting | Ease of Assembly

## Slide 39
DASHBOARD DESIGN
36
MAP, LAUNCH AND FAN BUTTON
SMS BUTTON
STARTER BUTTON
ETHERNET PORT

## Slide 40
CALCULATION OF DASHBOARD HEIGHT
37
Dashboard Location
Located such that driver's visibility os 20 feet ahead
Height decided such that sufficient clearance from floor for egress
Dashboard Height
27.08 inches

## Slide 41
38
Pedals mounted on chassis
Adjustable pedal assembly to incorporate all drivers
Design and assembly was made robust for fast changing
All forces from pedals dissipating into chassis
Appropriate height for comfort of drivers
Driver can reach and actuate the pedals
Goals
PEDAL ASSEMBLY DESIGN

## Slide 42
PEDAL ASSEMBLY DESIGN
1
2
3
290mm HEIGHT OF PEDAL
ADJUSTABILITY OF 50mm, 25mm FORE AND 25mm AFT
PROVIDE RAISED HEIGHT
39

## Slide 43
FUTURE GOALS
40
1
Hybrid Chassis
2
Real time data of forces from Strain Gauges
Mathematical model to incorporate chassis stiffness, Weld Strength, Suspension Stiffness
3
4
Reduced Steering Effort and Ankle Strain